## Slide 1
Lakeland Amateur
Radio Club
March 11, 2024

## Slide 3
ANNOUNCEMENTS

## Slide 4
March 23rd
Heritage Day

## Slide 5
LARC Picnic
April 6ᵗʰ
Colt Creek State Park

## Slide 6
Sun N Fun
April 9-14

## Slide 7
Postponed TBD

## Slide 8
June 22-23

## Slide 11
What is APRS?
Automatic
Packet
Reporting
System

## Slide 12
  Invented by WB4APR Bob Bruninga (SK) in 1982 to plot Naval positions, first used as Connectionless Emergency Traffic System in 1984
  Data Mode
  Usually on 144.390 in the USA (can be on other frequencies)
  Can include GPS object location, weather, text messages, email, announcements, queries, and telemetry
  Was originally local but now can be digi-peated or even sent to/through the internet
  Built on AX-25 and is broadcast (fire and forget) as opposed to session based

## Slide 13
TNCs,
Digi-peaters,
and I-Gates
(Oh my!)

## Slide 14
Transceiver + TNC/Sound Card/Modem
Some radios all in one

## Slide 15
Transceiver + TNC/Sound Card/Modem
Some radios all in one
Can be radio plus TNC/Sound Card/Modem Hardware

## Slide 16
Transceiver + TNC/Sound Card/Modem
Some radios all in one
Can be radio plus TNC/Sound Card/Modem Hardware
Can be radio plus sound card plus software based TNC/modem

## Slide 17
DIGI-peater
Digital Repeater.

## Slide 18
DIGI-peater
Digital Repeater.
Polk is well covered by its APRS DIGI-peater network

## Slide 19
DIGI-peater
Digital Repeater.
Polk is well covered by its APRS DIGI-peater network
WC4PEM (Polk Emergency Management) and others contribute to a mesh network that covers most of Polk

## Slide 20
i-Gate
Internet Gateway

## Slide 21
i-Gate
Internet Gateway
Can be listen only or can also DIGI-peat/inject traffic from the internet.

## Slide 22
i-Gate
Internet Gateway
Can be listen only or can also DIGI-peat/inject traffic from the internet.

## Slide 23
i-Gate
Internet Gateway
Can be listen only or can also DIGI-peat/inject traffic from the internet.
This means traffic from one person can pass from one i-Gate to another i-Gate that has recently heard the intended recipient

## Slide 24
Most “beaconed” info can be found at the website aprs.fi

## Slide 27
DIGI-peater

## Slide 28
i-Gate

## Slide 29
Weather Station

## Slide 30
Winlink RMS Server

## Slide 31
Some Random Dude on a handheld

## Slide 32
Vehicles

## Slide 33
Echo-Link Connection

## Slide 34
RV telemetry!?!?!

## Slide 35
Event or special interest marker

## Slide 36
Positioning and Telemetry are just the tip of the iceberg
SMS messaging (https://aprs.wiki/SMS/)
Winlink (https://www.winlink.org/APRSLink)
Weather report message (https://sites.google.com/site/ki6wjp/wxbot0
and much more

## Slide 37
Thank
you!